## Slide 1: Let’s wake up

## Slide 2: TPUs, GPUs, CPUs and edge devices
Dr. Umberto Michelucci
umberto.michelucci@gmail.com
079 396 7406

## Slide 3: A bit of context

## Slide 4
Quelle: https://en.wikipedia.org/wiki/Moore%27s_law#/media/File:Moore's_Law_Transistor_Count_1970-2020.png

## Slide 5
Quelle: https://www.nextbigfuture.com/2019/02/the-end-of-moores-law-in-detail-and-starting-a-new-golden-age.html

## Slide 6
Diagram source: NAE Regional Meeting: https://sites.google.com/view/naeregionalsymposium
“Moore's law is the observation that the number of transistors in a dense integrated circuit doubles about every two years”. From Wikipedia

## Slide 7: To overcome the limitations we need to use task specific architectures
Task specific architecture: an architecture that does one thing and only one, but very efficiently.

## Slide 8: A CPU does the computation in a sequential process
Multiply-add operation on CPU. Credits for this image go to this Google Cloud article.

## Slide 9: A GPU parallelize many sequential processes
Multiply-add operation on GPU. Credits for this image go to this Google Cloud article.

## Slide 10: Tensor Processing Unit (TPU)

## Slide 11: TPU uses an architecture called systolic architecture
systolic execution architecture:
this works with data arriving at cells at regular intervals from different directions, more on that later. The computation can be carried out without accessing memory

## Slide 12: TPUs turn out to be very energy efficient
NAE Regional Meeting: https://sites.google.com/view/naeregionalsymposium

## Slide 13: Carbon footprint of training networks*
A single PC
Consider an Intel i7, according to specs it dissipates 95W → When working 24h it needs 2.28 kWh
GPU Nvidia 1080Ti, according to specs it dissipates 250 W → When working 24h it needs 6 kWh
A datacenter
Up to 5000 GPUs, CPU with 8 cores (ca. 10k CPUs) → 52.8 MWh (MEGA WATT PER HOURS PER DAY). A windmill produces roughly 12 MWh per day, that is enough for ca. 400-500 households...
* https://towardsdatascience.com/the-carbon-footprint-of-ai-research-812d9c974a5c

## Slide 14: TPU Limitations
Linear algebra programs that require frequent branching or are dominated by element-wise algebra;
Workloads that access memory in a sparse manner;
Workloads that require high-precision arithmetic;
Neural network workloads that contain custom TensorFlow operations written in C++, specifically, custom operations in the body of the main training loop.
Source: https://medium.com/sciforce/understanding-tensor-processing-units-10ff41f50e78

## Slide 15: TPU

## Slide 16: TPU
ASIC (Application Specific Integrated Circuit)

## Slide 17: Coral Edge TPU
ASIC (Application Specific Integrated Circuit)

## Slide 18: TPU version
Multiply-add operation on TPU. Credits for this image go to this Google Cloud article.

## Slide 19: Key enabler of the performance of TPUs
The key enabler is a major reduction of the von Neumann bottleneck.
The shared bus between the program memory and data memory leads to the von Neumann bottleneck, the limited throughput (data transfer rate) between the central processing unit (CPU) and memory compared to the amount of memory*.
* https://en.wikipedia.org/wiki/Von_Neumann_architecture#Von_Neumann_bottleneck

## Slide 20: Systolic matrix multiplication example
From: http://www.cs.hmc.edu/courses/2001/spring/cs156

## Slide 21: Systolic matrix multiplication example
b[2,0]
b[1,0]
b[0,0]
b[2,1]
b[1,1]
b[0,1]
b[2,2]
b[1,2]
b[0,2]
a[0,2] a[0,1] a[0,0]
a[1,2] a[1,1] a[1,0]
a[2,2] a[2,1] a[2,0]
t = 0

## Slide 22: Systolic matrix multiplication example
b[2,0]
b[1,0]
b[2,1]
b[1,1]
b[0,1]
b[2,2]
b[1,2]
b[0,2]
a[0,2] a[0,1]
a[1,2] a[1,1] a[1,0]
a[2,2] a[2,1] a[2,0]
t = 1
a[0,0]*b[0,0]
b[0,0]
a[0,0]

## Slide 23: Systolic matrix multiplication example
b[2,0]
b[2,1]
b[1,1]
b[2,2]
b[1,2]
b[0,2]
a[0,2]
a[1,2] a[1,1]
a[2,2] a[2,1] a[2,0]
t = 2
a[0,0]*b[0,0] +a[0,1]*b[1,0]
a[1,0]*b[0,0]
a[0,0]
b[1,0]
a[0,1]
b[0,1]
a[0,0]*b[0,1]
a[1,0]
b[0,0]

## Slide 24: Systolic matrix multiplication example
b[2,1]
b[2,2]
b[1,2]
a[1,2]
a[2,2] a[2,1]
t = 3
a[0,0]*b[0,0] +a[0,1]*b[1,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]
a[0,1]
b[2,0]
a[0,2]
b[1,1]
a[0,0]*b[0,1]+a[0,1]*b[1,1]
a[1,1]
b[1,0]
a[2,0]
a[0,0]
a[2,0]*b[0,0]
b[0,0]
b[0,1]
a[1,0]*b[0,1]
b[0,2]
a[0,0]*b[0,2]

## Slide 25: Systolic matrix multiplication example
b[2,2]
a[2,2]
t = 4
a[0,0]*b[0,0] +a[0,1]*b[1,0]+a[0,2]*b[2,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]+a[1,2]*b[2,0]
a[0,2]
b[2,1]
a[0,0]*b[0,1]+a[0,1]*b[1,1]+a[0,2]*b[2,1]
a[1,2]
b[2,0]
a[2,1]
a[0,1]
a[2,0]*b[0,0]+a[2,1]*b[1,0]
b[1,0]
b[1,1]
a[1,0]*b[0,1]+a[1,1]*b[1,1]
b[1,2]
a[1,0]*b[0,2]+a[0,1]*b[1,2]
a[2,0]*b[0,1]
a[1,0]*b[0,2]
a[2,0]
b[0,1]
b[0,2]
a[1,1]
a[1,0]

## Slide 26: Systolic matrix multiplication example
t = 5
a[0,0]*b[0,0] +a[0,1]*b[1,0]+a[0,2]*b[2,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]+a[1,2]*b[2,0]
a[0,0]*b[0,1]+a[0,1]*b[1,1]+a[0,2]*b[2,1]
a[2,2]
a[0,2]
a[2,0]*b[0,0]+a[2,1]*b[1,0]+
a[2,2]*b[2,0]
b[2,0]
b[2,1]
a[1,0]*b[0,1]+a[1,1]*b[1,1]+a[1,2]*b[2,1]
b[2,2]
a[1,0]*b[0,2]+a[0,1]*b[1,2]+a[0,2]*b[2,2]
a[2,0]*b[0,1]+a[2,1]*b[1,1]
a[1,0]*b[0,2]+a[1,1]*b[1,2]
a[2,1]
b[1,1]
b[1,2]
a[1,2]
a[1,1]
b[0,2]
a[2,0]
a[2,0]*b[0,2]

## Slide 27: Systolic matrix multiplication example
t = 6
a[0,0]*b[0,0] +a[0,1]*b[1,0]+a[0,2]*b[2,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]+a[1,2]*b[2,0]
a[0,0]*b[0,1]+a[0,1]*b[1,1]+a[0,2]*b[2,1]
a[2,0]*b[0,0]+a[2,1]*b[1,0]+
a[2,2]*b[2,0]
a[1,0]*b[0,1]+a[1,1]*b[1,1]+a[1,2]*b[2,1]
a[1,0]*b[0,2]+a[0,1]*b[1,2]+a[0,2]*b[2,2]
a[2,0]*b[0,1]+a[2,1]*b[1,1]+a[2,2]*b[2,1]
a[1,0]*b[0,2]+a[1,1]*b[1,2]+a[1,2]*b[2,2]
a[2,2]
b[2,1]
b[2,2]
a[1,2]
b[1,2]
a[2,1]
a[2,0]*b[0,2]+a[2,1]*b[1,2]

## Slide 28: Systolic matrix multiplication example
t = 7
a[0,0]*b[0,0] +a[0,1]*b[1,0]+a[0,2]*b[2,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]+a[1,2]*b[2,0]
a[0,0]*b[0,1]+a[0,1]*b[1,1]+a[0,2]*b[2,1]
a[2,0]*b[0,0]+a[2,1]*b[1,0]+
a[2,2]*b[2,0]
a[1,0]*b[0,1]+a[1,1]*b[1,1]+a[1,2]*b[2,1]
a[1,0]*b[0,2]+a[0,1]*b[1,2]+a[0,2]*b[2,2]
a[2,0]*b[0,1]+a[2,1]*b[1,1]+a[2,2]*b[2,1]
a[1,0]*b[0,2]+a[1,1]*b[1,2]+a[1,2]*b[2,2]
b[2,2]
a[2,2]
a[2,0]*b[0,2]+a[2,1]*b[1,2]+
a[2,2]*b[2,2]

## Slide 29: Systolic matrix multiplication example
Done
a[0,0]*b[0,0] +a[0,1]*b[1,0]+a[0,2]*b[2,0]
a[1,0]*b[0,0]+a[1,1]*b[1,0]+a[1,2]*b[2,0]
a[0,0]*b[0,1]+a[0,1]*b[1,1]+a[0,2]*b[2,1]
a[2,0]*b[0,0]+a[2,1]*b[1,0]+
a[2,2]*b[2,0]
a[1,0]*b[0,1]+a[1,1]*b[1,1]+a[1,2]*b[2,1]
a[1,0]*b[0,2]+a[0,1]*b[1,2]+a[0,2]*b[2,2]
a[2,0]*b[0,1]+a[2,1]*b[1,1]+a[2,2]*b[2,1]
a[1,0]*b[0,2]+a[1,1]*b[1,2]+a[1,2]*b[2,2]
a[2,0]*b[0,2]+a[2,1]*b[1,2]+
a[2,2]*b[2,2]

## Slide 30: Example of Google Cloud TPU v2
2 systolic array of 128x128 ALU (Arithmetic Logical Units), for 32,768 ALUs for 16 bit floating point values in a single processor.

## Slide 31: Limitations of the Google Coral TPU

## Slide 32: Components that are needed in the Coral TPU
The Coral TPU supports only INT8 number format. The output of the TPU is floating point.

## Slide 33: Reading material
In-Datacenter Performance Analysis of a Tensor Processing Unit
https://arxiv.org/abs/1704.04760

## Slide 34: TensorFlow Lite - a primer

## Slide 35: Mobile and embedded devices
Definition of Embedded Devices: An embedded device is an object that contains a special-purpose computing system. The system, which is completely enclosed by the object, may or may not be able to connect to the Internet.
Generally, an embedded device's operating system will only run a single application which helps the device to do its job. Examples of embedded devices include dishwashers, banking ATM machines, routers, point of sale terminals (POS terminals) and cell phones. Devices that can connect to the Internet are called smart or intelligent. If an embedded device can not connect to the Internet, it is called dumb.

## Slide 36: What are the limitations of embedded devices
Because embedded systems have limited computing resources and strict power requirements, writing software for embedded devices is a very specialized field that requires knowledge of both hardware components and programming.

## Slide 37: What are the main objectives we must keep in mind
Model size
We need a small model (file) size to reduce possible download time and RAM usage.
Latency, Battery and heat
We need to reduce amount of computations needed for inference
Other constraints
We may have additional constraints. For example no UI or user interaction. Or slow computational power.

## Slide 38: Process to use a model on the edge
Train and save a model (development machine)
Convert the model (development machine)
Copy the converted model on the device
Run inference with the TF Lite interpreter

## Slide 39: Main reason to convert a model
The main reasons to convert the model are
Make it smaller (smaller memory footprint)
Make inference more efficient
Require less memory access
Use less energy in inference
To achieve those goals the main component is what is called QUANTIZATION.

## Slide 40: Quantization

## Slide 41: Quantization
Source: https://sahnimanas.github.io/post/quantization-in-tflite/#deep_compression

## Slide 42: Quantization and overflow
Source: https://sahnimanas.github.io/post/quantization-in-tflite/#deep_compression

## Slide 43: There two types of quantization
Post-training quantization - more simple and easier to implement and in most cases extremely efficient
Training-aware quantization - more complex that require the re-writing of the computational graph (see for example https://github.com/tensorflow/tensorflow/tree/r1.13/tensorflow/contrib/quantize)

## Slide 44: How TensorFlow lite quantize
Per-axis (aka per-channel in Conv ops) or per-tensor weights are represented by int8 two’s complement values in the range [-127, 127] with zero-point equal to 0. Per-tensor activations/inputs are represented by int8 two’s complement values in the range [-128, 127], with a zero-point in range [-128, 127].
Source: https://www.tensorflow.org/lite/performance/quantization_spec
Activations are asymmetric (zero point anywhere in the range)
Weights are symmetric (zero point where the original zero is) (we don’t need to multiply by zero, and the weights that are zero remains zero)

## Slide 45: Deployment of a model on a device
Source: https://www.tensorflow.org/lite/convert/index#device_deployment

## Slide 46: An introduction to TF Lite

## Slide 47: TensorFlow lite converter
import tensorflow as tf
converter = tf.lite.TFLiteConverter.from_saved_model(saved_model_dir)
tflite_model = converter.convert()
open("converted_model.tflite", "wb").write(tflite_model)

## Slide 48: TensorFlow Lite converter
The converter generates a TensorFlow Lite FlatBuffer*
Why flatbuffers? Two of the main reasons are:
Access to serialized data without parsing/unpacking
Memory efficiency and speed - The only memory needed to access your data is that of the buffer.
Cross platform code with no dependencies
* FlatBuffers is an efficient cross platform serialization library for C++, C#, C, Go, Java, JavaScript, Lobster, Lua, TypeScript, PHP, Python, and Rust. It was originally created at Google for game development and other performance-critical applications. [https://google.github.io/flatbuffers/]

## Slide 49: Post-training Quantization

## Slide 50: Post-training Quantization decision tree
Source: https://www.tensorflow.org/lite/convert/index#device_deployment
Google Coral TPU
You cannot quantize the inputs if you have never seen them.

## Slide 51: Quantization strategies
Source: https://www.tensorflow.org/lite/performance/post_training_quantization
Google Coral TPU

## Slide 52: Hybrid quantization - floating point to 8-bits (weight quantization)
import tensorflow as tf converter = tf.lite.TFLiteConverter.from_saved_model(saved_model_dir) converter.optimizations = [tf.lite.Optimize.OPTIMIZE_FOR_SIZE] tflite_quant_model = converter.convert()
At inference, weights are converted from 8-bits of precision to floating point and computed using floating-point kernels. This conversion is done once and cached to reduce latency.
Source: https://www.tensorflow.org/lite/performance/post_training_quantization

## Slide 53: Full integer quantization of weights and activations
To do this, you need to measure the dynamic range of activations and inputs by supplying a representative data set. You can simply create an input data generator and provide it to the converter.
The resulting model should be fully quantized, but any ops that do not have quantized implementations are left in floating point. This allows conversion to occur smoothly, but the model won't be compatible with accelerators that require full integer quantization. Additionally, the model still uses float input and output for convenience.
Source: https://www.tensorflow.org/lite/performance/post_training_quantization

## Slide 54: Full integer quantization of weights and activations
import tensorflow as tf
def representative_dataset_gen(): for _ in range(num_calibration_steps): # Get sample input data as a numpy array in a method of your choosing. yield [input] converter = tf.lite.TFLiteConverter.from_saved_model(saved_model_dir) converter.optimizations = [tf.lite.Optimize.DEFAULT] converter.representative_dataset = representative_dataset_gen tflite_quant_model = converter.convert()

## Slide 55: Full integer quantization of weights and activations
To ensure compatibility with some accelerators (such as the Coral Edge TPU), you can enforce full integer quantization for all ops and use integer inputs and outputs
Source: official TensorFlow lite documentation

## Slide 56: Full integer quantization of weights and activations*
converter.target_spec.supported_ops = [tf.lite.OpsSet.TFLITE_BUILTINS_INT8] converter.inference_input_type = tf.uint8 converter.inference_output_type = tf.uint8 converter.experimental_new_converter = True
* This has been tested with TF version 2.2.0-dev20200113

## Slide 57: Compile a model for the Edge TPU
To run a model on the Coral Edge TPU one needs two components:
A model quantized for UINT8 (restricted to operations that support UINT8)
The compiled version of the quantized model
edgetpu_compiler [options] model...

## Slide 58: Demo 1 - Size comparison
→ Folder Bootcamp-Deep-Learning-on-Edge-Devices/profiling
# python MobileNetV2_mode_size_comparison.py
-rw-r--r-- 1 umberto staff 14621440 Jan 14 13:57 mobilenetv2.h5
-rw-r--r-- 1 umberto staff 13978380 Jan 14 13:57 mobilenetv2.tflite
-rw-r--r-- 1 umberto staff 3579720 Jan 14 13:57 mobilenetv2_opt.tflite

## Slide 59: Effect of TPU
TPU
13.0ms
1.2ms
1.2ms
1.2ms
1.1ms
1.1ms
1.1ms
1.1ms
0.5ms
0.4ms
CPU
38.0ms
37.7ms
37.8ms
37.7ms
37.7ms
37.7ms
37.7ms
37.7ms
37.7ms
37.7ms
4 layer, each 1024 neurons; MNIST classification; ReLU Activation functions; inference running time

## Slide 60: The effect of TPU is not always evident
If the operations are between small matrices, you will not see any difference!

## Slide 61: Hands-on session (1/4) https://colab.research.google.com/drive/1v18ICGO9ccTfyo2fKzMbiq9XgQ4zvLik

## Slide 62: Hands-on session (2/4) https://colab.research.google.com/drive/1ob7AexaeWiaQiFWWuak4agcMxXiL0ms7

## Slide 63: Hands-on session (3/4) https://colab.research.google.com/github/google-coral/tutorials/blob/master/retrain_classification_ptq_tf2.ipynb#scrollTo=srOYhMYfx9XH

## Slide 64: Hands-on session (3/4) NOTE: this demo is the same as (2/4) with the only difference that it uses a different network. https://colab.research.google.com/drive/1NsrA_ABfVulXRfs3HgKvKZyggVuJG0oM